## Slide 1: Prestige NAND Flash DOWNLOAD

## Slide 2
Prepare ＩＴＥＭ.
PC
- Run Tftpd32 program.
(Tftpd32-3.28-setup.exe install )
2. Download DVR B/D
3. Download Serial B/D
4. LAN CABLE
After Download, Please update New Final Firmware.

## Slide 3
File need to download
Make a PC C:\tftpserver. Folder and copy files
No Space in Between. Any name possible
Ex) c:\tftpsever -> O
c:\tftp sever -> X
kernel_pr_09 -> 4/8/16 Kerrnel File
PR#3r#20110314.jffs2 -> 4/8/16CH RootFS image file

## Slide 4
1. Assign C:\tftpserver
2. Diaable
PC IP Address
3. 1,2 Process, and OK
RUN Tftpd32 Server
- The program must be in running when download firmware to DVR board

## Slide 5
DVR Main B/D & Serial Connected
* Warnning Cable must be in right direction !!!
Ex) 16cH M/B
Pin 1
(GND)

## Slide 6
RUN Hiper Terminal
Start  All Programs  Accessories  Communications  Hiper Terminal
Bitrate  115200
Data bit  8
Parity  None
Stop  1
Flow Control  None

## Slide 7
Set IP Address
After Power on, enter Ctrl-C to to abort booting
Enter “6”
Enter IP address “192.168.101.254”
Enter Gateway “192.168.101.1”

## Slide 8
Erase RootFS area
After Power on, enter Ctrl-C to to abort booting
Enter “5”
Enter “nand erase nobad 0x30700000 0x03800000” this takes 1 minutes
Enter “Exit”

## Slide 9
Flash kernel
After Power on, enter Ctrl-C to to abort booting
Enter “y”
Enter “2”
Enter “192.168.101.206”
Enter “kernel_pr_09”

## Slide 10
Flash root file system
After Power on, enter Ctrl-C to to abort booting
Enter “a”
Enter “2”
Enter “192.168.10.230”
Enter “PR#3r#20110314.jffs2”

## Slide 11: End Reboot DVR